## Slide 1: Qupls4: Instruction Cache
System Bus 256b
Cache Controller
Cache RAM
256 x 512b
Even Lines
Cache RAM
256 x 512b
Odd Lines
Even / Odd swapper
Instruction Aligner
4 x 2 to 1 Mux
Instr 1
Instr 2
Instr 3
Instr 4
Instr 1
Instr 2
Instr 3
Instr 4
Branch NOPs
Two 256b bus cycles are run by the cache controller to full-fill a 512b cache miss request.
Depending on the instruction pointer value an even, odd or odd, even pair of cache lines is selected.
On a cache miss the entire cache line is NOPed out.
A pair of cache lines is selected to allow instructions to span cache-line boundaries. Since instructions are 48-bit they do not fit evenly into a cache-line.
The instruction aligner right aligns instructions based on the IP value so that only four instruction decoders are required. Four instructions are selected plus a raw portion of the cache-line to allow for decoding immediates.
For branch miss, a set of NOPs is fed into the pipeline causing a pipeline bubble.
Cache miss NOPs

## Slide 2: Qupls4: Instruction Fetch Stage (*_fet)
NOP mux
Raw instruction cache output
1024b
1024b
Cache miss
Pipeline Register
The primary function of the fetch stage is to register the instruction cache output which is unregistered.
If there is a cache miss, NOPs are inserted into the pipeline.
Two 512-bit cache lines are fetched to allow instructions to span a cache line.

## Slide 3: Qupls4: Instruction Extract Stage (*_mux)
Instruction Aligner
PC[5:1]
Cache line in 1024
Extract
Ins #0
Extract
Ins #1
Extract
Ins #2
48
48
48
Branch Decode #0
Branch Decode #1
Branch Decode #2
48 + 240
raw
48 + 240 raw
48 + 240 raw
To next PC logic
Four Instructions plus cache line to decode stage
The cache line is fed in and right aligned according to the PC value.
Four instructions are extracted from the right.
Branch instructions are decoded to feed the next PC logic
Both instructions and raw cache line data are passed to the decode stage.
Raw cache line data is to detect constant zones.
Pipeline Register
1024b cache line pair from instruction fetch stage
48
Extract
Ins #3
Branch Decode #3
48 + 240 raw

## Slide 4: Qupls4: Decode Stage (*_dec)
µop 0
µop 1
µop 31
µop 30
µop Buffer
ISA Instruction To µop map
ISA Instruction To µop map
ISA Instruction To µop map
8 max
8 max
8 max
µop
Decoder
µop Decoder
µop Decoder
1
1
1
1
1
1
Four instructions from Extract Stage
1
1
1
Four decode busses to Rename Stage
Every clock cycle four micro-ops are decoded and sent to the rename stage.
The micro-op buffer is shifted right by four micro-ops. When the buffer has four or fewer micro-ops left in it, a request is made to the extract stage for more instructions.
Incoming instructions are mapped very quickly onto one to eight micro-ops.
Micro-ops are stored in the buffer; between four and thirty-two micro-ops will fill the buffer.
Micro-ops are packed as they are stored in the buffer so there are no “holes”.
Instruction Request
Pipeline Register
1
µop Decoder
1
ISA Instruction To µop map
8 max
1

## Slide 5: Qupls4: Decode Stage (more)
µop 0
µop 1
µop 31
µop 30
µop Buffer
Constant
Decoder
Constant Decoder
Constant Decoder
1
1
1
3
3
3
Twelve constants to Rename Stage
Cache line from decode (512 bits)
Indexes to cache line constants are decoded from the micro-ops and the cache line.
There may be three cache line constants per micro-op.
Pipeline Register
µop Rd
Decoder
µop Rd Decoder
µop Rd Decoder
1
1
1
Four destination names to Rename Stage
Name Supplier
1
1
1
Pipeline Register
The destination register from each micro-op decoder is fed to the name supplier which supplies a rename for the register.
1
Constant Decoder
3
µop Rd Decoder
1
1

## Slide 6: Qupls4: Rename Stage (*_ren)
RAT – Register Alias Table
1
1
1
Four pairs of destination registers and corresponding renames from decode stage.
Asynchronous Architectural Register to Physical Register Mapping Process
12 micro-op Window
4
ROB – Reordering Buffer
1
1
1
Four micro-ops with constants from Decode Stage
Pipeline Register
4
The register alias table is updated with info from the decode stage.
An asynchronous process matches unmapped architectural registers to physical register and maps them.
Micro-op and constants are enqueued in the re-order buffer
1
1

## Slide 7: Qupls4 Rename Stage
Rename Lookup:
16 source rename ports
4
4
4
4
Registe File
4
4
4
4
Rename Stage Pipeline Register
4
4
4
4
Decode stage outputs, source register specs.
Register File Output: 16 operand values
rf_reg = prn
If the register file contained a valid value, the operand is marked valid and does not need further updates. Otherwise, the operand is not valid and will be validated by the reservation station.
Operands looked up include:
argA – first source operand
argB – second source operand
argC – third source operand
argT – destination operand (as a source)
Note that instructions may have three more operands:
argD – fourth source operand (fused dot-products)
argS – floating-point status register
argT2 – second destination operand (floating-point stat).
The second set of operands is supplied by a prefix instruction as these operands are often not needed.

## Slide 8: Qupls4: Execute Stage
Bitfield
FSQRT
FDIV
FPU
SAU #0
SAU #1
IMUL
IDIV
FDP #0
TRIG
CSRs
Counts
Shift
ISQRT
FDP #1
FCU
AGEN #0
AGEN #1
DRAM #0
DRAM #1
13:52 rotating mux/demux
4
3
3
2
4
3
5
5
2
2
1
1
13
Read from register file
2
1
1
2
2
2
2
1
1
1
22 Flow through result queues (32 entry)
24:4 rotating multiplex
4 results
Write to register file
Pipeline Register
SAU: Simple Arithmetic Unit (integer and float)
IMUL: Integer multiplier
IDIV: Integer Divider
FMA: Floating-point multiply and add
TRIG: Floating-point trig, divide and square root
FCU: Flow control unit (branch unit)
AGEN: Address generator
DRAM: Data cache control logic
Read ports are packed into a vector containing only
source operands that need reading.
4
2
Lat: 1
Lat: 1
Lat: 4
Lat: 8
Lat: 8
Lat: ??
Lat: 1
Lat: 3
Lat: ??
Neural Network
16 parallel neurons
3
1
Port Packing
13
Rotating muxes change the read/write port priority every clock cycle to prevent ports from starving.
There is bypassing from register file inputs to reservation stations.
Reservation stations have three entry input queues.
Crypto
1
1
Register File Read
Reservation Stations
Graphics
3
1
Capabilities
2
3
3
Hardware Queues

## Slide 9: Qupls4: Reservation Stations
Operand Latch #1
Operand Latch #2
Operand Latch #3
Operand Latch #4
Queue Entry #1
Operand Latch #1
Operand Latch #2
Operand Latch #3
Operand Latch #4
Queue Entry #2
Operand Latch #1
Operand Latch #2
Operand Latch #3
Operand Latch #4
Queue Entry #3
3:1 mux
Operands
To Functional Unit
Bypass Network
Register File
A request is made to the register file to fetch values that have not been latched yet.
Operand latches are filled from either the register file or the results bypassing network as available.
Once all operands are valid for a queue entry, the instruction may be scheduled to go to the functional unit. The functional unit must also be ready to accept a new operation.
Once the queue entry has gone to the functional unit it is marked available for a new instruction.
Scheduler
Register Read Request

## Slide 10
Root Opcode Map
Orange = control
Yellow = capabilities
Grey = arithmetic
Green = branch
Pink = memory
There are about 25 open opcodes and the instruction set is pretty complete. There may be some more graphics or AI instructions to be added yet.

## Slide 11: Qupls4: External Interrupt Handling
Deferred IRQ FIFO
Processor Pipeline
If IRQ disabled at time of commit
The IRQ is deferred by a FIFO
Branch Target Buffer Logic
Mux
Incoming IRQ
Control Logic
Front-end: Next IP
The CPU chooses the deferred IRQ FIFO as the source of interrupts if there is any interrupt in the FIFO, otherwise the external interrupt feeds the branch-target buffer.
The incoming interrupt acts like a branch and directly changes the IP causing immediate fetch of ISR instructions.
However, if the IRQ should have been disabled, then it is recorded in the deferred FIFO and not immediately processed.

## Slide 12: Qupls4: MSI Interrupt Logging
CPU
CPU
CPU
CPU
Response Bus
MSI Logger
Request Bus to Memory
The MSI Interrupt Logger snoops the CPU response bus to detect interrupts and logs them to an area of memory.
The Logger acts as a bus master and is capable of filtering interrupts which were destined for a particular CPU.
It may also filter responses based on interrupt priority level.
Snoop bus

## Slide 14: Qupls4: QMSI Interrupt Controller Site
CPU
CPU
CPU
CPU
Response Bus
QMSI IRQ Controller
The QMSI Interrupt Controller snoops the CPU response bus from the system to detect interrupts.
Detected interrupts are queued in the controller in up to 63 priority queues.
The output of the priority queues are fed to the selected cores according to the affinity mask for the interrupt.
Up to 63 CPU cores may be connected to one QMSI IRQ controller.
Snoop bus
IRQ Bus

## Slide 15: Qupls4: Decoding Placement
Instruction Cache
Instruction (ISA) Align and Extract
Instruction to Micro-op Translator
Micro-op Decoder
Register Rename Stage
Instruction Queue to Re-order Buffer
Instruction Dispatcher
Reservation Stations
Reservation Stations
Reservation Stations
Reservation Stations
Functional Units
Micro-op decode
Decoding
Most of the decode takes place in two places. Between micro-op translation and register rename, and in the functional units

## Slide 16: Qupls4: Data Cache
Cache RAM 512 x 512b x 4 way
Tag RAM
512 x 48b x 4 way
Cache Controller
System Bus
256b wide
Data Aligner
Two 256b bus cycles are run by the cache controller to full-fill a 512b cache miss request.
The data aligner shifts the data into or from the proper position on the cache line.
Up to 512b Data

## Slide 17: Qupls4: Reorder Buffer
ROB Entry
ROB Entry
ROB Entry
ROB Entry
ROB Entry
ROB Entry
ROB Entry
ROB Entry
The reorder buffer is a circular queue with at least 16 entries (not all entries shown below).
Each ROB entry contains information needed to manage the progress of the instruction (micro-op).
Instructions are added at the tail location and committed from the head location.
The head and tail rotate with the tail always behind the head.

## Slide 18: Qupls4: QMSI Interrupt Cycle
QMSI interrupt cycles may occur at any point. They are ignored by a bus master and picked up by the QMSI interrupt controller instead. They are single cycle events.
Active cycle
QMSI IRQ
The presence of a QMSI interrupt during an active bus cycle causes the master to delay negating the cycle until after the QMSI interrupt is no longer present. This is to allow the master to capture the incoming data
instead of the QMSI message.
Inactive bus, master ignores QMSI
Response bus acknowledge
1 clock delay

## Slide 19
Execute
Q+4 Block Diagram
L1 I-Cache
32kB – 4 way
Fetch
128B cache line pair
Align
48x4= 192 Bits = 24B
Extract x4
Decoder x4
Rename x4
Reorder Buffer 16 to 64 Entries
Scheduling
SAU #0
SAU #1
FCU
MEM 0
CSRs
FPU
Neural Net
GP File
Arch. Regs
40 x 64b
Physical Register File
512 x 64b
IMUL
TRIG
Load / Store Queue
8 Entries
L1 Data Cache
64kB – 4 way
BTB 512 Entries
Instruction Pointers
gselect
predictor
TLB L1: 8 Entry – 8 way
TLB L2: 1024 Entry – 3 way
32B
System Bus
System Bus
32B
TLB L1: 8 Entry – 8 way
TLB L2: 1024 Entry – 3 way
(Same TLB as above)
Vector File
Arch. Regs
32 x 256b
Count
Shift
Bitfield
IDIV
ISQRT
FDP #0
FDP #1
FDIV
FSQRT
Crypto
MEM 1
Graphics
Capabilities
Dispatch x4
Reservation Stations
Result Queues
Rotating Mux
To Register File

## Slide 20: Qupls4: Streams
IP
Group header
Stream #
IP Offset
Micro-op
Re-order entry
Since instructions are fetched in groups from the same instruction pointer address, the IP address is stored in the group header for the instruction group. This conserves bits over storing the IP with each instruction.
The offset from the IP is stored for each instruction of the group in the re-order entry along with the stream number and micro-op among other things. The LSB of IP offset is not stored since it is always zero. So, the IP offset field contains one of 0,3,6,9,… multiples of three up to the machine width. Currently up to six bits are stored.
The stream number is a synonym for a branch checkpoint index; five bits are allowed for which allows for 32 streams. More than 16 streams does not improve performance; however, that is for a single thread. The streams are shared between all threads.
Whenever a new stream is needed (for a conditional branch) it is allocated and added to the dependency list of the active stream. The new stream inherits all the dependencies of the active stream. An X*Y dependency map is generated with newly allocated streams added to the map. Each row of the map represents the dependencies of a given stream. When a stream is freed up the row is marked empty with no dependencies. Computing the stream dependency map can be done quickly.
The stream number is used when a branch resolves to invalidate the instructions that are not along the correct path. The stomp logic takes the ‘good’ stream as input and traces though all the dependent streams branching out from the good stream that are to be stomped on. Therefore, the stomp logic generates a list of dependent streams that are not to be taken.
The stomp logic then compares the stream in the pipeline registers and the stream in the re-order buffer for each bank of instructions to the listed entries. If a stream is found on the list it is stomped on. Doing the compare can be done fast, it is just checking a bit in a dependency list bitmap.
Stream #
IP Offset
Micro-op
Re-order entry
Re-order entry
…

## Slide 21: Qupls4: Read Port Selector
16 Ports
48Ports
These ports are from the rename stage available when the instruction is queued or dispatched. (4 insn x 4 ports)
These ports are “catch up” ports from the reservation stations for when the values were not available at queue/dispatch time.
16 Ports
8 Ports
These are physically statically connected to the register file.
Six groups of eight ports
Round-robin arbiter
Selects one group from six

## Slide 22: Qupls4: Dispatch
Fetch
Extract
Decode
Rename
Re-order buffer
Dispatch
Out-of-order
Issue
In-order stages
Execute
Commit
Out-of-order dispatch does not stall the pipeline when execution units are busy (queues full).
With out-of-order dispatch instructions may be dispatched again by resetting bits in the ROB.
The execute unit may need more operands than are supplied by a single micro-op. (REXT) The REXT prefix is performed out-of-order.

## Slide 23: Qupls4: Name Supplier
Bitmap1
Bitmap2
Bitmap3
Bitmap4
Select
Freed tag
Delay Line (16 cycles)
The name supplier uses four bitmaps, each bitmap containing flags for the physical registers.
Each bitmap represents ¼ of the physical register tags.
A register tag is chosen from each bitmap as needed to supply rename tags.
When a tag is freed, it is placed at the end of a delay line so that it may not be selected until the delay (16 cycles) expires.
Delaying the availability of free tags prevents pipelining issue resulting from a tag being reused too quickly.
Commit stage
Tag request
(Rename)
Re-order buffer

## Slide 25
Execute
Q+4 Block Diagram
L1 I-Cache
32kB – 4 way
Fetch
128B cache line pair
Align
48x4= 192 Bits = 24B
Extract x4
Decoder x4
Rename x4
Reorder Buffer 16 to 64 Entries
Scheduling
XPIPE 0
GP File
Arch. Regs
128 x 64b
Physical Register File
512 x 64b
(12 read / 6 write)
Load / Store Queue
8 Entries
L1 Data Cache
64kB – 4 way
BTB 512 Entries
Instruction Pointers
gselect
predictor
TLB L1: 8 Entry – 8 way
TLB L2: 1024 Entry – 3 way
32B
System Bus
System Bus
32B
TLB L1: 8 Entry – 8 way
TLB L2: 1024 Entry – 3 way
(Same TLB as above)
Dispatch x6
Execution Pipelines x6
6x Results to Register File
XPIPE 1
XPIPE 2
XPIPE 3
XPIPE 4
XPIPE 5

## Slide 26: Qupls4: Execute Stage
Bitfield
ALU
ALU
IMUL
IDIV
FMA
TRIG
CSRs
Counts
Shift
ISQRT
FMA
AGEN
MEM
4
3
12
Read from register file
1
6 Results
To regfile
Write to register file
ALU: Arithmetic Logic Unit (integer and float)
IMUL: Integer multiplier
IDIV: Integer Divider
FMA: Floating-point multiply and add
TRIG: Floating-point trig, divide and square root
FCU: Flow control unit (branch unit)
AGEN: Address generator
MEM: Memory (Data cache control logic)
Read ports are packed into a vector containing only
source operands that need reading.
4
1
Lat: 1
Lat: 1
Lat: 5
Neural Network
16 parallel neurons
Port Packing
12
Rotating muxes change the read port priority every clock cycle to prevent ports from starving.
There is bypassing from register file inputs to reservation stations.
Reservation stations have three entry input queues.
Register File Read
Reservation Stations
Graphics
Hardware Queues
1
ALU
IMUL
AGEN
MEM
4
1
1
FRCPA
Insn
Queue
Insn
Queue
Insn
Queue
4
Insn
Queue
3
Insn
Queue
Lat 5
ALU
ALU
ALU
1
Crypto
Insn
Queue
Branch
Cap.
6 Results Bypass
Crypto
Branch
Cap.
CSRs
Counts
Shift
FMA
Graphics
Hardware Queues
FRCPA
Neural Network
16 parallel neurons
ISQRT
TRIG
IDIV
FMA
Bitfield