## Slide 1: Qupls4: Constants
Small constants are often embedded in the instruction.
6-bits for arithmetic type instructions
16-bits for arithmetic immediate mode type instructions
16-bits for scalar load / store displacements
6-bits for vector load / store displacements
When a larger constant is needed it follows the instruction on the cache-line in a constant zone.
Constant Zones
  Constant zones are special NOP instructions that contain constant data. Multiple constant zones may be concatenated together to form a much larger zone. A constant zone up to 240 bits in size is possible (six zone instructions).
Zone40
NOP8
Zone40
NOP8
Zone40
NOP8
Instr41
OP7
Instructions contain six-bit codes for referencing constants in the constant zone following the instruction
Two bits indicate the size of the constant
Four bits indicate the offset of the constant in the combined zone, the constant offsets are multiples of 16-bits.
A single instruction may reference multiple constants in the zone.
There may be more than one constant in a zone instruction.
Constants may span multiple zone instructions.
…

## Slide 2: Qupls4: Constants
Constants in the zone may be 16,32,48 or 64-bits in size.
Zone40
NOP8
Zone40
NOP8
Zone40
NOP8
Zone40
NOP8
Zone160
Constant zones are concatenated together by the CPU to form a large zone that may be indexed into.
The combined zone may be up to 240-bits in size. This is enough room for 3x64 plus 1x48 bit constant.
Zone160
Constants may span zone instructions and are always 16-bit aligned within the zone.
Constant64
Constant16
Constant16
Constant64