## Slide 1: Qupls4: Unconditional Branches
JMP Instr.
Instr 3
Instr 1
Instr 4
Instr 2
Instr 3
Instr 1
Instr 4
Lead instruction of MUX group
The instructions following an unconditional jump or branch at the decode stage are made invalid. Because instructions are fetched in groups of four, the two trailing instructions are the next sequential instruction and not the desired destination instructions.
If the branch target buffer (BTB) predicted correctly, the lead instruction of the MUX group will begin at the branch’s destination address. The jump instruction will effectively have no delay.
If the BTB prediction was incorrect, the the front-end of the pipeline is invalidated. This includes the align, fetch, multiplex and decode stages. The address for the next instruction fetch is set to the jump address. This will take at least four clock cycles (16 instructions are invalidated).
Unconditional branches (BSR or JSR) with only a displacement have the destination calculated in the decode stage.