## Slide 1: Qupls4: Instruction Cache
System Bus 256b
Cache Controller
Cache RAM
256 x 512b
Even Lines
Cache RAM
256 x 512b
Odd Lines
Even / Odd swapper
Instruction Aligner
4 x 2 to 1 Mux
Instr 1
Instr 2
Instr 3
Instr 4
Instr 1
Instr 2
Instr 3
Instr 4
Branch NOPs
Two 256b bus cycles are run by the cache controller to full-fill a 512b cache miss request.
Depending on the instruction pointer value an even, odd or odd, even pair of cache lines is selected.
On a cache miss the entire cache line is NOPed out.
A pair of cache lines is selected to allow instructions to span cache-line boundaries. Since instructions are 48-bit they do not fit evenly into a cache-line.
The instruction aligner right aligns instructions based on the IP value so that only four instruction decoders are required. Four instructions are selected plus a raw portion of the cache-line to allow for decoding immediates.
For branch miss, a set of NOPs is fed into the pipeline causing a pipeline bubble.
Cache miss NOPs

## Slide 2: Qupls4: Instruction Fetch Stage (*_fet)
NOP mux
Raw instruction cache output
1024b
1024b
Cache miss
Pipeline Register
The primary function of the fetch stage is to register the instruction cache output which is unregistered.
If there is a cache miss, NOPs are inserted into the pipeline.
Two 512-bit cache lines are fetched to allow instructions to span a cache line.

## Slide 3: Qupls4: Instruction Extract Stage (*_mux)
Instruction Aligner
PC[5:1]
Cache line in 1024
Extract
Ins #0
Extract
Ins #1
Extract
Ins #2
48
48
48
Branch Decode #0
Branch Decode #1
Branch Decode #2
48 + 240
raw
48 + 240 raw
48 + 240 raw
To next PC logic
Four Instructions plus cache line to decode stage
The cache line is fed in and right aligned according to the PC value.
Four instructions are extracted from the right.
Branch instructions are decoded to feed the next PC logic
Both instructions and raw cache line data are passed to the decode stage.
Raw cache line data is to detect constant zones.
Pipeline Register
1024b cache line pair from instruction fetch stage
48
Extract
Ins #3
Branch Decode #3
48 + 240 raw

## Slide 4: Qupls4: Decode Stage (*_dec)
µop 0
µop 1
µop 31
µop 30
µop Buffer
ISA Instruction To µop map
ISA Instruction To µop map
ISA Instruction To µop map
8 max
8 max
8 max
µop
Decoder
µop Decoder
µop Decoder
1
1
1
1
1
1
Four instructions from Extract Stage
1
1
1
Four decode busses to Rename Stage
Every clock cycle four micro-ops are decoded and sent to the rename stage.
The micro-op buffer is shifted right by four micro-ops. When the buffer has four or fewer micro-ops left in it, a request is made to the extract stage for more instructions.
Incoming instructions are mapped very quickly onto one to eight micro-ops.
Micro-ops are stored in the buffer; between four and thirty-two micro-ops will fill the buffer.
Micro-ops are packed as they are stored in the buffer so there are no “holes”.
Instruction Request
Pipeline Register
1
µop Decoder
1
ISA Instruction To µop map
8 max
1

## Slide 5: Qupls4: Decode Stage (more)
µop 0
µop 1
µop 31
µop 30
µop Buffer
Constant
Decoder
Constant Decoder
Constant Decoder
1
1
1
3
3
3
Twelve constants to Rename Stage
Cache line from decode (512 bits)
Indexes to cache line constants are decoded from the micro-ops and the cache line.
There may be three cache line constants per micro-op.
Pipeline Register
µop Rd
Decoder
µop Rd Decoder
µop Rd Decoder
1
1
1
Four destination names to Rename Stage
Name Supplier
1
1
1
Pipeline Register
The destination register from each micro-op decoder is fed to the name supplier which supplies a rename for the register.
1
Constant Decoder
3
µop Rd Decoder
1
1

## Slide 6: Qupls4: Rename Stage (*_ren)
RAT – Register Alias Table
1
1
1
Four pairs of destination registers and corresponding renames from decode stage.
Asynchronous Architectural Register to Physical Register Mapping Process
12 micro-op Window
4
ROB – Reordering Buffer
1
1
1
Four micro-ops with constants from Decode Stage
Pipeline Register
4
The register alias table is updated with info from the decode stage.
An asynchronous process matches unmapped architectural registers to physical register and maps them.
Micro-op and constants are enqueued in the re-order buffer
1
1

## Slide 7: Qupls4: Execute Stage
Bitfield
FSQRT
FDIV
FPU
SAU #0
SAU #1
IMUL
IDIV
FDP #0
TRIG
CSRs
Counts
Shift
ISQRT
FDP #1
FCU
AGEN #0
AGEN #1
DRAM #0
DRAM #1
16:64 rotating mux/demux
4
3
3
2
3
3
4
4
2
2
1
1
16
Read from register file
2
1
1
2
1
1
2
1
1
1
16 Flow through result queues (32 entry)
20:4 rotating multiplex
4 results
Write to register file
Pipeline Register
SAU: Simple Arithmetic Unit (integer and float)
IMUL: Integer multiplier
IDIV: Integer Divider
FMA: Floating-point multiply and add
TRIG: Floating-point trig, divide and square root
FCU: Flow control unit (branch unit)
AGEN: Address generator
DRAM: Data cache control logic
Read ports are packed into a vector containing only
source operands that need reading.
3
1
Lat: 1
Lat: 1
Lat: 4
Lat: 8
Lat: 8
Lat: ??
Lat: 1
Lat: 3
Lat: ??
Neural Network
16 parallel neurons
3
1
Port Packing
16
Rotating muxes change the read/write port priority every clock cycle to prevent ports from starving.
There is bypassing from register file inputs to reservation stations.
Reservation stations have three entry input queues.
Crypto
1
1
Register File Read
Reservation Stations
Graphics
3
1
Capabilities
2
3
3
Hardware Queues

## Slide 8: Qupls4: Reservation Stations
Operand Latch #1
Operand Latch #2
Operand Latch #3
Operand Latch #4
Queue Entry #1
Operand Latch #1
Operand Latch #2
Operand Latch #3
Operand Latch #4
Queue Entry #2
Operand Latch #1
Operand Latch #2
Operand Latch #3
Operand Latch #4
Queue Entry #3
3:1 mux
Operands
To Functional Unit
Bypass Network
Register File
A request is made to the register file to fetch values that have not been latched yet.
Operand latches are filled from either the register file or the results bypassing network as available.
Once all operands are valid for a queue entry, the instruction may be scheduled to go to the functional unit. The functional unit must also be ready to accept a new operation.
Once the queue entry has gone to the functional unit it is marked available for a new instruction.
Scheduler
Register Read Request

## Slide 9
Root Opcode Map
Orange = control
Yellow = capabilities
Grey = arithmetic
Green = branch
Pink = memory
There are about 25 open opcodes and the instruction set is pretty complete. There may be some more graphics or AI instructions to be added yet.

## Slide 10: Qupls4: External Interrupt Handling
Deferred IRQ FIFO
Processor Pipeline
If IRQ disabled at time of commit
The IRQ is deferred by a FIFO
Branch Target Buffer Logic
Mux
Incoming IRQ
Control Logic
Front-end: Next IP
The CPU chooses the deferred IRQ FIFO as the source of interrupts if there is any interrupt in the FIFO, otherwise the external interrupt feeds the branch-target buffer.
The incoming interrupt acts like a branch and directly changes the IP causing immediate fetch of ISR instructions.
However, if the IRQ should have been disabled, then it is recorded in the deferred FIFO and not immediately processed.

## Slide 11: Qupls4: MSI Interrupt Logging
CPU
CPU
CPU
CPU
Response Bus
MSI Logger
Request Bus to Memory
The MSI Interrupt Logger snoops the CPU response bus to detect interrupts and logs them to an area of memory.
The Logger acts as a bus master and is capable of filtering interrupts which were destined for a particular CPU.
It may also filter responses based on interrupt priority level.
Snoop bus