## Slide 1: Qupls2026: Instruction Fetch Stage (*_fet)
NOP mux
Raw instruction cache output
1024b
1024b
Cache miss
Pipeline Register
The primary function of the fetch stage is to register the instruction cache output which is unregistered.
If there is a cache miss, NOPs are inserted into the pipeline.
A pair of cache lines is passed to the mux stage.

## Slide 2: Qupls2026: Instruction Extract Stage (*_mux)
Instruction Aligner
PC[5:1]
Cache line in 1024
Extract
Ins #0
Extract
Ins #1
Extract
Ins #2
40
40
40
Branch Decode #0
Branch Decode #1
Branch Decode #2
4x 2:1 Mux
66
66
66
66
66
66
Four Instructions from micro-code machine
To next PC logic
Cache line in 512
66
66
66
Four Instructions plus cache line to decode stage
The cache line is fed in and right aligned according to the PC value.
Five instructions are extracted from the right.
Instructions are fused into a 66-bit format.
Branch instructions are decoded to feed the next PC logic
Micro-code instructions are multiplexed onto the output.
Both instructions and cache line are passed to the decode stage.
Pipeline Register
512b cache line from instruction fetch stage
40
Extract
Ins #3
Branch Decode #3
66
66
66
40
Extract
Ins #4
Instruction Fuser

## Slide 3: Qupls2026: Decode Stage (*_dec)
µop 0
µop 1
µop 31
µop 30
µop Buffer
ISA Instruction To µop map
ISA Instruction To µop map
ISA Instruction To µop map
8 max
8 max
8 max
µop
Decoder
µop Decoder
µop Decoder
1
1
1
1
1
1
Four instructions from Extract Stage
1
1
1
Four decode busses to Rename Stage
Every clock cycle four micro-ops are decoded and sent to the rename stage.
The micro-op buffer is shifted right by four micro-ops. When the buffer has four or fewer micro-ops left in it, a request is made to the extract stage for more instructions.
Incoming instructions are mapped very quickly onto one to eight micro-ops.
Micro-ops are stored in the buffer; between four and thirty-two micro-ops will fill the buffer.
Instruction Request
Pipeline Register
1
µop Decoder
1
ISA Instruction To µop map
8 max
1

## Slide 4: Qupls2026: Decode Stage (more)
µop 0
µop 1
µop 31
µop 30
µop Buffer
Constant
Decoder
Constant Decoder
Constant Decoder
1
1
1
3
3
3
Twelve constants to Rename Stage
Cache line from decode (512 bits)
Indexes to cache line constants are decoded from the micro-ops and the cache line.
There may be two cache line constants per micro-op if the micro-op is a store instruction.
Pipeline Register
µop Rd
Decoder
µop Rd Decoder
µop Rd Decoder
1
1
1
Four destination names to Rename Stage
Name Supplier
1
1
1
Pipeline Register
The destination register from each micro-op decoder is fed to the name supplier which supplies a rename for the register.
1
Constant Decoder
3
µop Rd Decoder
1
1

## Slide 5: Qupls2026: Rename Stage (*_ren)
RAT – Register Alias Table
1
1
1
Four pairs of destination registers and corresponding renames from decode stage.
Asynchronous Architectural Register to Physical Register Mapping Process
12 micro-op Window
4
ROB – Reordering Buffer
1
1
1
Four micro-ops with constants from Decode Stage
Pipeline Register
4
The register alias table is updated with info from the decode stage.
An asynchronous process matches unmapped architectural registers to physical register and maps them.
Micro-op and constants are enqueued in the re-order buffer
1
1

## Slide 6: Qupls2026: Execute Stage
FSQRT
FDIV
FPU
SAU #0
SAU #1
IMUL
IDIV
FMA #0
TRIG
CSRs
Counts
Shift
ISQRT
FMA #1
FCU
AGEN #0
AGEN #1
DRAM #0
DRAM #1
12:36 rotating mux/demux
3
3
3
3
3
3
3
3
2
2
1
1
12
Read from register file
a,b,c
a,b,c
a,b,c
a,b,c
a,b,c
a,b,c
a,b,c
a,b,c
a,b
a,b
c
c
Fixed Channels Hi-lited in yellow
9 Fixed Channels, 26 rotating
11 Result Queues (32 entry)
12:4 rotating multiplex
4 results
Write to register file
Pipeline Register
SAU: Simple Arithmetic Unit (integer and float)
IMUL: Integer multiplier
IDIV: Integer Divider
FMA: Floating-point multiply and add
TRIG: Floating-point trig, divide and square root
FCU: Flow control unit (branch unit)
AGEN: Address generator
DRAM: Data cache control logic
3
a,b,c
Lat: 1
Lat: 1
Lat: 4
Lat: ??
Lat: 8
Lat: 8
Lat: ??
Lat: 1
Lat: 3